## Slide 1
Imperial College London · ELEC60014 · Group Project
In collaboration with NESO
CARBON INTENSITY RESEARCH · 2026
Mapping the Carbon
Cost of
Every Electron
on Britain's Grid
A nodal power flow model computing carbon intensity at every bus of the GB electricity network, hour by hour across an entire year, giving grid operators and investors unprecedented visibility into where emissions really come from.
2130
Network
buses modelled
8760
Hourly
snapshots · 2023
<1%
Error vs GB
actual output
41.1
Mean CI
gCO₂/kWh
THE PROBLEM
The UK grid must decarbonise at pace. But national average carbon intensity figures hide a critical truth: not all electrons are equal. Regional data tells you little about where investment in clean generation will have the greatest impact.
OUR SOLUTION
We built a full-year, nodal-resolution carbon intensity model using PyPSA-GB as the dispatch engine and Bialek average proportional sharing to attribute carbon to every node — validated against NESO's official Carbon Intensity API.
Mert · Annie · Ava · Matthew · Momo · Adnan
github.com/avagm/neso-carbon-intensity

## Slide 2
HOW IT WORKS
Nodal Carbon Intensity · GB Grid · 2023
THE PIPELINE
01
Dispatch Simulation
PyPSA-GB optimises generation dispatch across the full GB network using historical 2023 inputs - weather, demand, and generator capacity. Transmission losses (8%) and NESO's biomass emission factor (120 gCO₂/kWh) are explicitly modelled.
02
Bialek Tracing
Average proportional sharing traces power flows from each generator to each bus, assigning a precise carbon intensity to every node at every timestep — not just a system average. Runs across all 2,130 buses.
03
Validation
Nodal results are aggregated to NESO's 17 regional zones and compared against the official Carbon Intensity API. Annual generation output (272–273 TWh) sits within 1% of GB's reported 2023 consumption.
KEY RESULTS
272 TWh
Simulated annual generation
Within 1% of GB's actual 2023 consumption — energy balance confirmed across all 8,760 hourly snapshots.
0 gCO₂
Minimum nodal intensity
Wind & nuclear buses (SMAN11, SMAN12, RACW31) achieve zero carbon intensity during high renewable periods.
927 gCO₂
Maximum nodal intensity
WISD61 (coal-adjacent, SE England) records 22× the system average — invisible in regional figures.
NODAL CARBON INTENSITY — TOP AND BOTTOM 5 BUSES
▲ Highest emitting buses (mean CI, gCO₂/kWh)
WISD61
Coal-adjacent · SE England
926.5
NECH11
Gas OCGT · NE England
650.8
BRFO11
Mixed thermal · Scotland
508.5
ELLA11
Gas · East Midlands
492.7
MEDW41
CCGT · SE England
394.0
▼ Lowest emitting buses (mean CI, gCO₂/kWh)
HVDC_Ire…
Irish interconnector
0.0
RACW31
Wind-dominated bus
0.0
WERW31
Wind-dominated bus
0.0
SMAN11
Nuclear / wind cluster
0.0
SMAN12
Nuclear / wind cluster
0.0
WHY THIS MATTERS
National CI figures mask a 900+ gCO₂/kWh spread between the cleanest and dirtiest nodes on the GB grid. Without nodal resolution, grid investment decisions, carbon contracts and demand-response strategies are flying blind.
Target clean investment where it reduces emissions most
Enable location-aware carbon contracts and pricing
Support NESO regional reporting with validated nodal data
Open-source and reproducible - built on PyPSA-GB
Mert · Annie · Ava · Matthew · Momo · Adnan
Imperial College London · ELEC60014 · May 2026
github.com/avagm/neso-carbon-intensity
In collaboration with NESO