## Slide 1
NESO CARBON INTENSITY PROJECT
Imperial College London · ELEC60014 · 2026
Mapping GB Carbon Intensity
How network resolution reshapes Britain's carbon map, from a single-node copperplate to 2,000 buses, benchmarked against NESO across full-year 2023.
ETYS 2,000-bus catchment view, 2023 (provisional). Green = clean, red = carbon-intensive.
In collaboration with the National Energy System Operator
02
TWO WAYS TO MAP A TOPOLOGY
NESO regions vs Voronoi catchments
The same Reduced 32-bus dispatch, mapped two ways. NESO aggregates buses into 14 statutory reporting regions; Voronoi catchments tessellate GB by nearest bus, keeping every one of the 32 buses distinct.
› Both show the generation view, where emitting plant sits. Scotland (wind, nuclear) stays green; Yorkshire and the south (gas, waste) run hot. › Aggregating to regions hides the within-region spread the catchment view keeps.
Reduced 32-bus · generation view · full year 2023
03
VALIDATION
Benchmarked against NESO, hour by hour
Adding network constraints sharpens the hourly fit: RMSE falls 38.0 to 28.3 gCO2/kWh from copperplate to 32-bus. ETYS 2000-bus (provisional) sits highest, a real congestion signature plus an interior-point solve still being tightened.

## Slide 2
04
HOW IT WORKS
From dispatch to carbon intensity
1
NESO pull National carbon intensity plus published emission factors: the reference series.
2
PyPSA-GB solve Linear-program economic dispatch on each topology, full-year 2023, Gurobi.
3
Carbon intensity NESO factors applied to dispatched generation, summed every hour.
4
Align Hourly UTC, model against NESO, 8,713 matched hours of 2023.
5
Compare Heatmap and interactive dashboard across the four topologies.
Default settings: no demand uplift, linear dispatch (no unit commitment), Gurobi LP, pinned PyPSA-GB commit 074ea25e. Every result is regeneratable from the repo.
Emission factors (gCO2/kWh): wind/solar/nuclear 0 · biomass 120 · CCGT 394 · coal 937
PyPSA-GB · NESO Carbon Intensity API · Gurobi
05
THE TEAM
Who built this
An Imperial College London EEE group project (ELEC60014), in collaboration with the National Energy System Operator.
Mert
Annie
Ava
Matthew
Momo
Adnan
Open-source and reproducible, built on PyPSA-GB.
4
topologies
2,130
buses (ETYS)
8,760
hours
github.com/avagm/neso-carbon-intensity
Imperial College London · May 2026
06
IN SUMMARY
What the comparison shows
› Network detail matters: 32-bus constraints lift annual-mean intensity by ~10 gCO2/kWh over an unconstrained copperplate. › 17 and 32 bus agree on the annual mean (within 2 gCO2/kWh) but differ hour to hour by ~16 on average. › Reduced 32-bus tracks NESO best: R 0.936, RMSE 28.3 gCO2/kWh. › Full ETYS 2,000-bus (provisional) carries a real congestion signature: +37 gCO2/kWh vs NESO.
Disclaimer Independent academic study using PyPSA-GB and the NESO Carbon Intensity API. Results are the authors' own and are not produced, endorsed, or validated by NESO. Under default settings (no demand uplift, linear dispatch) the modelled series sit 7 to 9 gCO2/kWh below NESO; the study isolates network topology, not a match to NESO. ETYS 2,000-bus is a provisional interior-point solve.
Full year 2023 · PyPSA-GB commit 074ea25e · gCO2 per kWh throughout.
github.com/avagm/neso-carbon-intensity